## Slide 1
Work
Shouldn't be...
Shocking!

## Slide 2: VOLTAGE, CURRENT, & RESISTANCE
VOLTAGE – unit of measurement of electromotive force (EMF)
CURRENT - Continuous movement of electrons past a given point. (measured in amperes)
RESISTANCE – Opposition to movement of electrons. Makes it possible to generate heat, control current flow, & supply correct voltage to devices

## Slide 3: OHM’S LAW
George Simon Ohm
  Formulated a mathematical relationship between:
    Current
    Voltage
    Resistance
  Resistance = Impedance
    Resistance = DC
    Impedance = AC
    Interchangeable – Most Branch circuits

## Slide 4: DIRECT CURRENT
Always flows in one direction
Used to charge batteries, run some motors, operate magnetic lifting devices and welding equipment.

## Slide 5: ALTERNATING CURRRENT
More common in electrical work
Changes rapidly in both direction and value
Power companies produce power cheaper with alternating current

## Slide 6: What does hazard mean?
Hazard means:
any potential or actual threat to the wellbeing of people, machinery or environment
Electrical hazard safety means:
taking precautions to identify and control electrical hazards

## Slide 7: Why know about it?
Because failing to take the necessary precautions can lead to:
injury or death
fire or property damage

## Slide 8: What are the safety priorities?
Electrical hazards exist in almost every workplace. Common causes of electrocution are:
making contact with overhead wires
undertaking maintenance on live equipment
working with damaged electrical equipment, such as extension leads, plugs and sockets
using equipment affected by rain or water ingress

## Slide 9: ELECTRICAL HAZARDS
SHOCK. Electric shock occurs when the human body becomes part of the path through which current flows.
The direct result can be electrocution.
The indirect result can be injury resulting from a fall or movement into machinery because of a shock

## Slide 10: ELECTRICAL HAZARDS
BURNS. Burns can result when a person touches electrical wiring or equipment that is energized.
ARC-BLAST. Arc-blasts occur from high- amperage currents arcing through the air. This can be caused by accidental contact with energized components or equipment failure.

## Slide 11: ELECTRICAL HAZARDS
ARC-BLAST. The three primary hazards associated with an arc-blast are:
Thermal radiation.
Pressure Wave.
Projectiles.

## Slide 12: ELECTRICAL HAZARDS
EXPLOSIONS. Explosions occur when electricity provides a source of ignition for an explosive mixture in the atmosphere.

## Slide 13: ELECTRICAL HAZARDS
FIRES. Electricity is one of the most common causes of fires both in the home and in the workplace. Defective or misused electrical equipment is a major cause.

## Slide 14: EFFECTS ON THE HUMAN BODY
Depends on:
Current and Voltage
Resistance
Path through body
Duration of shock

## Slide 15: Effects
Protection
  Circuit Breakers
  Fuses
  15 or 20 amps
  Property/equipment protection

## Slide 16: What are the levels of effect of current?
AC current (mA) | Effect on human body
1 | Slight tingling sensation
2-9 | Small shock
10-24 | Muscles contract causing you to freeze
25-74 | Respiratory muscles can become paralysed; pain; exit burns often visible
75-300 | Usually fatal; ventricular fibrillation; entry & exit wounds visible
>300 | Death almost certain; if survive will have badly burnt organs and probably require amputations

## Slide 17: Conductors
American Wire Gauge
  12 gauge – 20 amps (Safely)
  14 gauge – 15 amps
  10 gauge – 30 amps
What determines amount of amps through a circuit?
  How much the equipment draws
  How much “stuff” plugged in

## Slide 18: Wires
Black = hot = Ungrounded Conductor
White = neutral = Grounded Conductor (connected to grounding electrode/Grounding rod)

## Slide 20: How to check
Wiring Checks
  Testers
  Different types

## Slide 21: What should you do in an electrical emergency?
For low voltage electricity >50 V AC and 110 V DC
remove the source of electricity supply
commence CPR if trained
call the emergency number on site
For high voltage electricity >1000 V
call the emergency number for your site
don’t go near the casualty
don’t touch the casualty or try to free them with anything

## Slide 22: What should you do in an electrical emergency?
For low voltage electricity >50 V AC and 110 V DC
remove the source of electricity supply
commence CPR if trained
call the emergency number on site
For high voltage electricity >1000 V
call the emergency number for your site
don’t go near the casualty
don’t touch the casualty or try to free them with anything

## Slide 23: Can you protect yourself from electricity?
Don’t wear metal objects
Turn power off
Wear appropriate clothing
Don’t touch live parts
Don’t install or repair electrical equipment
Use qualified personnel
Clean and dry leads and plugs before use
Use PPE

## Slide 24: What are other safety measures?
Heed warning signs
Use the right equipment
Study the operation manual
Take care of extension leads
Use only approved extension lamps
Don’t pull on leads
Use residual current devices – RCDs
Use the proper fuses and circuit breakers

## Slide 25: Regular safety inspections
are a part of YOUR job...
Electrical equipment should be checked each time before use for defects
If not tagged or the tag is out of date then report it and place it out of service

## Slide 26
Is it Safe?
What do you think?
Could you make this a better installation?