## Slide 1: Construction Basics

## Slide 2: Planning the Housing Site
One of the first points to consider is the housing site, the specific parcel of land the house will sit on.
The natural conditions of the site can influence how the home is situated on the lot. A small lot won’t have space for a large one-story home but a two-story house would work well.
Local zoning laws affect how the site is used. Such as how far the house must be from the property lines.

## Slide 3: Analyzing Characteristics of the Site
Topography: the contour, or slope, of the land and it’s other physical features.
Land that is flat, well-drained, and free of rocks is generally the easiest and least expensive to build on.
Be sure to visit the site when it is raining to check for drainage problems.

## Slide 4: Planning the Orientation
Orientation: its position on the lot and the direction the home faces.
A home oriented to receive maximum sunlight will need less artificial lighting.
In regions with cold winters, exposure to the sun is especially important.
The south and west sides of a dwelling receive the most sunlight.
Rooms that are the center of family activity (kitchen & family room) are best located on the south or west side.

## Slide 5: Planning the Orientation
Homes also need protection from the hot summer sun.
  -An overhanging roof or awning may help provide shade.
In warm climates, a dwelling should be oriented so that it takes advantages of breezes.
Cross-ventilation: air flow created when air travels in one side of the home and out the other.
In areas of cold winters, homes should be protected from strong, north winds . Few windows on the north side of the home.
Rows of trees and shrubs may be planted around a home to act as a windbreak.

## Slide 6: Architectural Drawings
Floor plan: a scale diagram of one or more rooms as if seen from above.
A basic floor plan includes info about the size and location of walls, doors, windows, stairs, closets, fireplaces, cabinets, and major appliances.
There may be separate floor plans for the electrical, plumbing, and heating and cooling systems.

## Slide 7: Architectural Drawings
Elevation: shows vertical surfaces as if viewed by someone standing on the ground or on the floor.
Many architects use computer-aided design (CAD) programs to generate drawings.
Symbols are used as a type of building short-hand.
See Fig. 10-6 on page 222 for common architect symbols

## Slide 8: The Basic Structure
The Foundation:
  - The underlying base and support of a home. It consists of the footing and the foundation.
  -Footing: a continuous concrete base that supports the foundation walls below ground level.
  -footings should be placed on solid, undisturbed soil below the frost line (the depth to which frost penetrates soil in the area the house is built).
  -if footings are placed above the frost line, the soil under them could freeze and expand, causing the foundation to crack.

## Slide 9: 3 Types of Foundation
1. Basements
2. Crawl Spaces
  -has about 18 to 24 inches of space between the ground and the bottom floor of the home.
3. Slabs
  -does not have a basement or crawl space
  -parts of the plumbing and heating systems are put in place before the slab is poured

## Slide 10: The Frame
The skeleton of the housing structure
If the frame is not constructed properly, the structure may sag or even collapse
Most home framing is done with wood or engineered wood products.
Steel framing is more expensive
Steel can withstand termites, fire, and severe weather and will not shrink or settle over time.

## Slide 11: The Floor Frame
First piece attached to the foundation wall is the sill plate.
Floor frame consists of girders, joists, ridging and subflooring.
In parts of the country where termites are common, a termite guard should also be installed.
  Termite guard: a metal shield fastened on the top of the foundation walls under the sill. It prevents termites from getting into the wood structure of the building.

## Slide 12: The Wall Frame
The wall frame is built on top of the floor frame
The wall frame supports the ceiling, upper floors, and roof and serves as a nailing base for wall finishes.
Standard construction uses 2X4 wood studs placed every 16 inches.
Load-bearing walls: an interior wall which supports the floors and roof above. A load-bearing wall should never be removed unless a beam is put up to take its place.
Nonbearing wall: an interior wall that does not support any weight from the structure. It may be removed

## Slide 13: The Ceiling and Roof Frames
The roof frame consists of a series of rafters that support the weight of the roof.
The slope of the rafters establishes the roof pitch.
The steeper the slope of the roof, the less likely it is to leak.
On most roofs the rafters extend past the edge of the exterior wall to provide an overhang. This prevents water from running down the walls and also shades the home.

## Slide 14: Finishing the Exterior Walls
Rough boarding or sheathing is applied to the outside of the roof and wall framing.
  -it is usually 4x8 foot panels
  -generally moisture-resistant
  -helps brace the frame against wind by joining the floor framing and studs
  -can consist of:
  -plywood
  -foam
  -oriented strand board (OSB): made from strands of wood fibers that are bonded together with water-resistant adhesives

## Slide 15: The Walls
After sheathing is up, builders usually wrap the home with a heavy waterproof material.
  -keeps out water and moisture
  -reduces heat loss by keeping insulation dry
  -closes the small cracks and holes in the rough boarding to keep out wind.

## Slide 16: The Final Exterior Finish
The most common materials used
  -wood
  -aluminum
  -vinyl
Wood
  -strong, a good insulator, easy to assemble, and suitable for a wide variety of exterior styles.
  OSB and plywood siding is a popular alternative to the high cost of wood.

## Slide 17: The Final Exterior Finish
Manufactured Siding
  -made of aluminum or steel is durable and resists weather and corrosion
  -helps lower heating and cooling costs
  -aluminum does dent and may conduct electricity
  -steel is dent-resistant and one of the most durable siding materials
  -vinyl fairly durable and requires no maintenance. Less likely to dent & doesn’t conduct electricity. However it is brittle and more likely to crack or break under extreme weather conditions.
  -Vinyl and aluminum can be dented and damaged in hailstorms.

## Slide 18: The Final Exterior Finish
Masonry Siding includes:
  Brick
  Clay
  Tile
  Stone
  Concrete block
  Stucco: a plaster material made with cement, sand and lime
Masonry construction is often more expensive than wood construction but usually less expensive to maintain and lasts longer.

## Slide 19: The Final Exterior Finish
Paints and Finishes
  -Siding made of wood products must be protected against the elements.
  -This can be done by painting or staining and sealing the wood.
  -OSB siding MUST be painted
  -primer should be applied to exterior wood before painting

## Slide 20: The Final Exterior Finish
Water-based paints
  -expand with changing temperatures without cracking the paint
  -easy to spread, dry quickly, and have good color retention
Oil-based paints
  -harder to spread
  -take longer than water-based paint to dry
  -hide imperfections better than water-based paint
  -many are harmful to the environment

## Slide 21: The Roof
Light-colored roofs are popular in hot climates because they help keep the home cool by reflecting sunlight. It can reduce cooling needs by 20 to 50 percent.
Shingles
  -thin pieces of material laid in overlapping rows.
  -asphalt shingles are used most widely
  -wood shingles and shakes(a thicker shingle) are attractive but may cost 50 to 100 percent more than asphalt shingles

## Slide 22: The Roof
Slate and tile
  -in places with hot sun and little snowfall roofs are covered with clay tile, slate or concrete tile.
  -are fireproof and make the strongest roofing material
  -in cold climates they tend to crack
Steel
  -very durable and provide excellent protection against severe weather, even hail.
  -can last longer than 50 years
  -initial cost is higher than shingles but lasts twice as long

## Slide 23: Installing the Roof
Roof frame is covered with sheathing, then roofing felt, then shingles or tiles.
Flat roofs are not shingled. Instead building paper is applied with a special compound and then covered with gravel. Most practical in areas where there’s little or no snow.
Flashing (strips of sheet metal) is installed where the roof meets a vertical surface such as a chimney, skylight s, second story wall etc. (see pg. 231). Flashing prevents moisture from leaking through roof openings and insulates the roof from heat from a chimney.

## Slide 24: Insulation
Purpose of insulation is to reduce the passage of heat through the walls and roof.
Effectiveness depends on the R value. This is a measure of its capacity to resist winter heat loss and summer heat gain.
The higher the R value, the better the insulation. The R value is given per inch.
The R value of exterior walls can vary from R-9 to R-24. Ceiling R Values- R-30 to R-49. Floor R Values- R-13 to R-25.

## Slide 25: Vapor Barriers
Materials that help reduce drafts and prevent moisture from getting into a home.
Forms of Insulation
Flexible insulation
  -blanket
  - covered with paper on one side and a vapor barrier material on the other side
  -bat (blanket insulation cut into shorter lengths)
  -often uncovered and made of fibrous material such as fiberglass

## Slide 26: Forms of Insulation (cont.)
Loose-Fill Insulation
  -can be poured, blown in, or packed by hand
  -care must be taken to distribute loose-fill evenly and to replace the insulation when it begins to break down with age.
Foam Insulation
  -pumped through a tube to the location where it is to be applied.
  -expands after application to fill all cracks and crevices
  -typically easier to install, safer for the environment, and more energy efficient than traditional batt insulation

## Slide 27: Forms of Insulation (cont.)
Rigid Insulation
  -rigid foam panels that can serve as rough wall boarding as well as insulation
Reflective Insulation
  -such as aluminum foil, tin-coated sheet metal, and coated paper
  -very effective in keeping heat from entering a home so they are more likely to be used in warmer climates.

## Slide 28: Window Frames
Wood has been commonly used for window frames and sashes
All wood frames are generally more expensive
Aluminum and vinyl window frames are light-weight and come in a variety of factory finishes and designs. They are easy to install and remove
Metal frames conduct heat and cold so wood frames are better insulators than metal frames

## Slide 29: Types of Glass
A single thickness of glass is a poor insulator
2 or 3 panes sealed together is a better insulator
Low-emissivity (low-e) glass has a clear coating that helps keep heat inside in winter and outside in summer.
Low-e glass blocks ultraviolet rays and helps reduce fading of upholstery fabrics and drapes.
May not be desirable in the south windows of a home designed for passive solar heating because it does block the sun more

## Slide 30: Types of Glass (cont.)
Tempered plate glass
  -extra strong glass
  -used for sliding glass doors because of its strength
Patterned glass/obscure glass
  -has a textured surface
  -allows light to pass through but no one can see through it
  -used for privacy purposes in bathroom windows or windows in exterior doors

## Slide 31: Doors
Made from wood, metal, fiberglass or a combination of these materials
Flush doors have a smooth surface
Panel doors have sunken or raised sections
Most doors come prehung in a wood or metal frame
Doors are either solid or hollow
  -hollow doors are lighter and generally used for interior doors
  -less expensive but also less sound-resistant
  -solid doors recommended for exterior doors for greater security and weather resistance

## Slide 32: Water Protection
Important to keep rainwater or melting snow from damaging the structure of the home
Finish Grade: finish level of earth next to the foundation. Should slope away from the home to prevent rainwater from seeping into the basement or crawl space.
Gutters and downspouts: prevents erosion of soil and damage to plants and shrubs close to a home and to carry rainwater away from the foundation of the home.

## Slide 33: The End