## Slide 1: Designing Homes for Today’s Needs

## Slide 2: Developing Communities
People have been planning communities for hundreds of years.
During colonial times, villages often grew up around a village green.
Government buildings, churches and shops were centrally located around the green.
Today, development continues at a fast pace.
Managing rapid growth without drawbacks is a goal of deliberate planning called smart growth.

## Slide 3: Building Laws & Regulation
Zoning Laws-laws that determine the type of building that may be constructed in a particular zone or section, of a community.
Restricted residential zoning: only single-family homes may be built
General residential zoning: allows apartment houses, town houses, two-family dwellings and some businesses and stores
Commercial zoning: stores and office buildings
Industrial zoning: factories and warehouses
Greenbelts: parklands and farmlands where no building is permitted

## Slide 4: Zoning Regulations
  May specify:
    Minimum lot size
    The distance a building may be from property lines or other buildings.
    Maximum heights of buildings.

## Slide 5: Building Codes
Rules that regulate the quality of building materials and set standards of quality and safety for construction
Can vary from area to area

## Slide 6: Building Codes
Regulate:
  Type and quality of building materials
  Form of construction
  -provisions for health, safety, and sanitation
  -Use of flammable materials
  -installation of fire exits
  -electrical work
  -type and installation of plumbing, heating, and ventilating systems

## Slide 7: Aesthetic Codes
Regulate the appearance of buildings in order to maintain the beauty and the desired look of an area.
Some HOAs restrict the exterior appearance of individual units such as certain colors.
In designated historic areas, homes must conform to standards set according to the time period in which the homes were constructed.
Resort communities have codes to protect the natural beauty of the area

## Slide 8: Planned Neighborhoods
The layout of the development, the type and appearance of housing units, and the use of surrounding land are all carefully planned before construction begins.
The locations of neighborhood schools, recreation, and shopping area also determined in advance.
  Cluster Homes: groups of homes clustered together on a development site and surrounded by open spaces or forested land
  Zero-lot-line homes: placed on the lot line rather than on the center of the lot, gives each home more usable yard space

## Slide 9: Master Planned Communities
Take the planned neighborhood concept one step further, creating developments that are virtually self-contained towns.
These communities feature housing, shops, public spaces such as parks, libraries, and community centers.
« Walkable » neighborhoods where residents can walk down the street to mail a letter, buy groceries, or go to the movie.

## Slide 10: Cooperative Housing Communities
Balance the traditional advantages of home ownership with the benefits of shared common facilities such as a large dining room, meeting rooms, recreational areas, workshops, and child care.

## Slide 11: Housing Reflects Changing Needs
Social trends help shape people’s housing needs.
Some rooms featured in yesterday’s homes are no longer used for the same purposes. Ex: formal parlors now family rooms, cellars for storing food now refrigerators and freezers
Now rooms are multipurpose rooms
Home offices are common now, not in the past

## Slide 12: Home Zones
Private zone: provides quiet, comfortable areas for sleeping and relaxing, as well as privacy for bathing and dressing.
Service zone: where household work is done. It includes the kitchen, laundry room, workshop, or garage may also be part of service zone.
Social zone: used for activities and entertainment. Living room, dining room, family room, recreation room, entryway, patio etc.

## Slide 13: Open & Closed Floor Plans
Closed Plan: rooms are separated and self-contained. Allows for greater privacy and better separation between zones.
Open Plan: When few dividing walls separate rooms. Seems more spacious, offers flexibiity for entertaining.

## Slide 14: Evaluating a Floor Plan
Look at the floor plan
Evaluate the traffic pattern, the paths people take as they walk from room to room during everyday activities.
Easy access should be provided between closely related areas. Ex: kitchen to dining area
Economy of construction-costs can be reduced if two areas that require plumbing, such as kitchen and laundry areas, are placed back-to-back.

## Slide 15: One-Level Homes
All parts of the living area are easily accessible without going up or down stairs.
Eliminating stairs also increases the usable space in the home.
Exterior maintenace of a one-story house, such as painting, cleaning-gutters, etc., is easier than on a two-story home.
Generally has more universal design appeal
Disadvantage: requires more space to build, increases the cost of the lot, foundation, and roof construction

## Slide 16: Two-Level Homes
Advantages
Easier to separate private zones from other zones since most two-level homes put the bedrooms on the second floor.
Uses less space
Disadvantage:
Stairs must be climbed to reach the bedrooms

## Slide 17: Split-Level Homes
Uses space efficiently
Multiple levels allow for good separation between zones yet only a few steps are required to go from one level to another

## Slide 18: Split-Entry Homes
Has two levels of living space with the lower level partially below the ground.
The main entrance to the home is located midway between the two main levels.
Persons entering a foyer area must go either up or down a short flight of stairs to reach one of the main levels.
No part of the house is accessible to someone who cannot climb stairs.

## Slide 19: Recent Trends in Housing Design
Energy efficient and environmentally friendly homes
Front porches are becoming popular again
Outdoor areas as an extension of the living space
Laundry areas on the second floor
Media rooms
Bonus rooms

## Slide 20: The End