## Slide 1: Developing a Design Plan

## Slide 2: Steps in a Design Plan
Identify the design goal
Assess client characteristics
Analyze the environment
Develop a preliminary budget
Compile a design resource file
Plan use of space
Choose a style and color scheme
Select backgrounds, furniture, lighting, and accessories
Present the design
Implement the design

## Slide 3: Good Design Requires Planning
The design will be more successful if you lay a foundation for the project.
Following the process helps designers develop pleasing rooms that meet the clients’ needs.
Design Process should be followed regardless of the size of the design project. Even a small project can turn out to be more expensive than it should if it is not planned carefully.

## Slide 4: Step 1: Identify the Design Goal
A designer’s initial task is to help clients clearly identify the design goal.
To develop a realistic plan, the budget needs to be determined
The desired time frame should also be assessed
  It’s realistic to expect a room to be painted in a week but not realistic to expect a kitchen remodel in a week.

## Slide 5: Step 2: Assess Client Characteristics
Success in a design project begins with matching possibilities for the room design with the habits, likes, needs, and wants of the people who will use it.
Designers usually use one or more inventories-(surveys that identify characteristics that will affect the design plan).

## Slide 6: Step 2: Assess Client Characteristics
Family Inventory should discuss:
  -Lifestyle
    -Activities: how will the room be used?
    -Entertaining Preferences: will the room be used for entertaining? If so, formal or informal? Usual number of guests? Entertainment-related equipment needed?
    -Hobbies: Does the family have hobbies that might require special storage needs?
    -Study and Work: Where do family members prefer to read? Study? Pay bills? How many computers do they need? Etc.

## Slide 7
  -Preferred Atmosphere
  -What are the family’s overall style preferences? Rustic or traditional? Sleek and stylish or soft and cozy? Antiques or modern look? What are their color preferences?
  -Future Considerations
  -Once a room is completed, it’s apt to stay that way for some time. So the family should consider changes that might occur in the future such as adding a pet or adding to the family.

## Slide 8: Nonresidential Inventories
Purpose of the room
Characteristics of the people who will use it and their needs
Universal design should always be considered

## Slide 9: Step 3: Analyze the Environment
The Environment Inventory assess the following factors:
  -Number and Placement of Rooms
  -Activity Zones, identify the current private, social and service zones of the home. Do they need improved?
  -Storage Areas: is there adequate storage?
  -Furniture and Accessories-access the current furniture, is it in good condition, will it work in the new design?

## Slide 10: Step 3: Analyze the Environment
Environment Inventory (cont.)
  -Condition of Backgrounds: try to gauge not only the condition, but also the appeal, of the current flooring, walls, and window treatments
  -Energy Considerations: Keep energy efficiency in mind when assessing an environment
  -Electrical and Lighting: Is the home’s electrical service adequate for existing lighting and equipment? Is the lighting sufficient for the new design?

## Slide 11: Step 3: Analyze the Environment
Environment Inventory (cont.)
  -Safety: For homes with young children or elderly think about features such as childproofing, grab bars, etc.
  -Traffic Flow: Does furniture placement make the current traffic pattern awkward? Is furniture too large for the space? Is there adequate clearance space (the additional space furniture takes up when it’s in use).

## Slide 12: Step 3: Analyze the Environment (cont.)
Consider Furniture Needs
  -Know the number and types of pieces you want to incorporate in the floor plan
Establish Priorities
  -The designer can help clients prioritize, or rate their wants and needs in order of preference to figure out what the client hopes to achieve.
Make a scale drawing of the room and furniture that will go into the room. Include:
-doorways, windows, built-in cabinets, fireplaces, location of heating and cooling registers

## Slide 13: Step 4: Develop a Preliminary Budget
Include wall coverings, floor coverings, window treatments, fabric, furniture, lighting, and accessories.
Include labor for installing the above items.
Electricians, plumbers, and carpenters.
Have a contingency fee, an additional percentage of the total cost of the project, which might need to be used for unexpected expenses. A 20% contingency fee is often used.

## Slide 14: Step 4: Develop a Preliminary Budget
Visit local retail stores, review catalogs, search on the internet to determine realistic costs.
For wall, floor, and window coverings careful measuring and calculations are required.

## Slide 15: Measuring (pg. 458-459)
Paint
1. Measure the length of each wall, add the lengths together and total. (12 +12+30+30=84)
Multiply the length of feet around the room (answer from #1) by the height of the ceiling to determine the total number of square feet. (84 X 8 ft = 672 sq. ft.)
A gallon of paint will cover approximately 350 to 400 sq. ft. Divide the total number of square feet by 350 to find the number of gallons of paint. (672/ 350 = 2 gal. of paint)

## Slide 16: Measuring (pg. 458-459)
Wallpaper: follow Steps 1 and 2 as explained for paint.
1. Divide the total number of sq. ft. by 36. ( A single roll of wallpaper covers approximately 36 sq. ft.)
672 / 36 = 18.67 or 19 single rolls
2. For every two openings (doors and windows), subtract one roll of wallpaper. If the paper has a repeating pattern do not deduct for the openings.

## Slide 17: Measuring (pg. 458-459)
Resilient Flooring or Carpeting
  1. Measure the length of each wall and multiply the length by the width. (12 ft. x 30 ft.= 360 sq. ft.)
  2. Most carpet is sold by the square yard. To calculate that number, divide the total square feet by 9. (360/9=40 sq. yards)

## Slide 18: Measuring (pg. 458-459)
Window Treatments
  1. Measure the width and length of the area to be covered by the window treatment. (45 in. wide x 84 in. long)
  2. To give fullness to the window treatment, multiply the width by 2. If you are using a sheer fabric, multiply by 3
  (45 in x 2 = 90 inches)
  3. Determine the number of widths of fabric required by dividing the width including fullness (your answer from #2) by the width of the fabric. (Home decorating fabrics are often 54 inches wide.)
  (90 inches /54 in. = 1.67 or 2 widths of fabric

## Slide 19: Measuring Windows (cont. pg. 458-459)
  4. To determine the length of each width of fabric you must add 12 inches to the length of the window treatment. This is needed for the hem and the heading on the window treatment. (84 in. + 12 in. = 96 in. fabric required for each width
  5. Determine the total length of fabric required for the window treatment by multiplying the number of widths (your answer in #3) by the length of fabric required for each width (your answer in #4) 2 x 96 in. = 192 in. of fabric required

## Slide 20: Measuring Windows (cont. pg. 458-459)
  6. Fabric is sold in yards. You must convert the number of inches required into yards. Divide the length of fabric required for the window treatment (your answer in #5) by 36 in.
  192 in./36 in. = 5 1/3 yards of fabric

## Slide 21: Step 5: Compile a Design Resource File
Sources of Design Ideas
  -Decorating magazines
  -Furniture and accessory catalogs
  -Interior Design websites
  -Sunday newspapers run features on home design
  -How-to books and interior design reference books

## Slide 22: Things to Include in the Design Resource File:
Before and After photos
Photos of design ideas organized by rooms
Product brochures
Samples of wallpaper, paint and fabric

## Slide 23: The End